Using recent astrometry from Gaia/TGAS \citep{gaia2016a,gaia2016b}, with section filters parallax > 0, and parallax/parallax error >5, we integrated the galactic orbits for 898 s-process enhanced stars. Utilising the \texttt{gala} Python package \citep{price2017}, we integrated each star backwards for $0.5\,\textrm{Gyr}$ in a Milky Way-like potential that consists of four components: a \citet{hernquist1990} bulge and nucleus, a \citet{miyamoto1975} disk, and the \citet{nfw1997} halo. In this potential, the disk and bulge parameters were adjusted to be consistent with previous work \citep{bovy2015}. For our Gaia matched sample, we computed spatial velocities and galactic longitude and latitudes. Spatial velocities are relative to the local standard of rest, where U_{LSR} is positive towards the Galactic centre, V_{LSR} is positive in the direction of Galactic rotation (l=90^{\CIRC}, b=0^{\CIRC}), and W_{LSR} is positive towards the north galactic pole (b=90^{\CIRC}).

The majority of our sample showed pro-grade orbits that were consistent with membership in the Milky Way disk, indicating they do not originate from an unusual stellar event. Figure \ref{fig:figure4} illustrates the galactic position of each class of s-process enhanced star investigated. For our entire 898 sample, the figure shows \% reside within the galactic disk(\% thin disk and \% thick disk ), and % within the halo. Our results show similar trends to the literature, samples from \cite{gomez1997} and \cite{mennessier1997} present populations of 75\% contained within the disk, and 25\% within the halo. \cite{pereira2011}’s entire sample resides within the disk, and cite\{decastro2016} states their sample contains 90/% thin disk stars. Although, excluding \cite{decastro2016}’s sample, it is important to note previous studies contain limited stellar populations ranging from 4 to 12 stars, and cannot be representative of the overall galactic position of s-process enhanced stars. \cite{jorissen1993} attributes the galactic position of s-process enhanced stars as dependent on their intrinsic or extrinsic nature, given our sample is entirely extrinsic we cannot comment on the comparison between the two enhancement sources. However, given our extrinsically s-process enhanced sample concentrates towards the galactic plane, we can propose the sample in \cite{jorissen19993} was not large enough to represent the overall galactic position of extrinsic S stars.

toomre include in paper
L and b diagram, galactic longitude and lattitude
Lindegren et al. (2018): The astrometric solution;
Cropper et al. (2018): The Gaia Radial Velocity Spectrometer;
•
Sartoretti et al. (2018): Processing, validation and performance of the spectroscopic data;
•
Katz et al. (2018): Properties and validation of the radial velocities;

1. Gomez1997
   Conclusions:
   - Sample contains 4 group, 3 belonging to the disk and 1 belonging to the halo
   - luminosities of barium stars exist within a large range, from class Ib to IV-V, and most exhibiting that of normal giants, as consistent with the literature
   - Previously not undertaken, the author has obtained visual absolute magnitudes and kinematics
   - Two groups have been discriminated, a young and high luminosity, and main sequence/ subgiant stars

   Future prospects:
   - High res spectra needed to determine CNO and s-process abundances and to better discriminate between barium and non barium stars
2. Jorissen1993 Sect. 4.2
   Conclusions:
   - intrinsic S stars more concentrated towards the galactic plane in comparison to extrinsic S stars
   - made comment on most intrinsic S stars which have been observed for Tc are high-latitude objects, since they are the closest and thus brightest of the group … makes remark on bias of sample since intrinsic are brighter
   - similar spread to M giants from Michigan spectral catalog
   - extrinsic S stars are low-mass stars populating the RGB
   - derives scale height and absolute magnitude equation
   Future prospects:
   - not stated
Me
Integrate orbits
Spacial distribution
UVW velocities - galactic coordinate velocities (x,y) = (w, sqrt(u2+v2)) toomre diagram
Percentage in disk few in halo ect
Look at angmom in disk - how much theyre moving with the rest of the population
Eccentricity distribution
Two scripts 1. Integrate orbits with best values
                  2. Every star take uncertainties into account and integrate orbits